# Electromagnetic radiation
107 languages

- Article
- Talk

- Read
- Edit
- View history
Tools

From Wikipedia, the free encyclopedia

 linearly polarized electromagnetic wave going in the z-axis, with E denoting the electric field and perpendicular B denoting magnetic field
In physics, electromagnetic radiation (EMR) consists of waves of the electromagnetic (EM) field, which propagate through space and carry momentum and electromagnetic radiant energy.[1] Types of EMR include radio waves, microwaves, infrared, (visible) light, ultraviolet, X-rays, and gamma rays, all of which are part of the electromagnetic spectrum.[2]
Classically, electromagnetic radiation consists of electromagnetic waves, which are synchronized oscillations of electric and magnetic fields. Depending on the frequency of oscillation, different wavelengths of electromagnetic spectrum are produced. In a vacuum, electromagnetic waves travel at the speed of light, commonly denoted c. In homogeneous, isotropic media, the oscillations of the two fields are perpendicular to each other and perpendicular to the direction of energy and wave propagation, forming a transverse wave. The position of an electromagnetic wave within the electromagnetic spectrum can be characterized by either its frequency of oscillation or its wavelength. Electromagnetic waves of different frequency are called by different names since they have different sources and effects on matter. In order of increasing frequency and decreasing wavelength these are: radio waves, microwaves, infrared radiation, visible light, ultraviolet radiation, X-rays and gamma rays.[3]
Electromagnetic waves are emitted by electrically charged particles undergoing acceleration,[4][5] and these waves can subsequently interact with other charged particles, exerting force on them. EM waves carry energy, momentum and angular momentum away from their source particle and can impart those quantities to matter with which they interact. Electromagnetic radiation is associated with those EM waves that are free to propagate themselves ("radiate") without the continuing influence of the moving charges that produced them, because they have achieved sufficient distance from those charges. Thus, EMR is sometimes referred to as the far field. In this language, the near field refers to EM fields near the charges and current that directly produced them, specifically electromagnetic induction and electrostatic induction phenomena.
In quantum mechanics, an alternate way of viewing EMR is that it consists of photons, uncharged elementary particles with zero rest mass which are the quanta of the electromagnetic field, responsible for all electromagnetic interactions.[6] Quantum electrodynamics is the theory of how EMR interacts with matter on an atomic level.[7] Quantum effects provide additional sources of EMR, such as the transition of electrons to lower energy levels in an atom and black-body radiation.[8] The energy of an individual photon is quantized and is greater for photons of higher frequency. This relationship is given by Planck's equation E = hf, where E is the energy per photon, f is the frequency of the photon, and h is Planck's constant. A single gamma ray photon, for example, might carry ~100,000 times the energy of a single photon of visible light.
The effects of EMR upon chemical compounds and biological organisms depend both upon the radiation's power and its frequency. EMR of visible or lower frequencies (i.e., visible light, infrared, microwaves, and radio waves) is called non-ionizing radiation, because its photons do not individually have enough energy to ionize atoms or molecules, or break chemical bonds. The effects of these radiations on chemical systems and living tissue are caused primarily by heating effects from the combined energy transfer of many photons. In contrast, high frequency ultraviolet, X-rays and gamma rays are called ionizing radiation, since individual photons of such high frequency have enough energy to ionize molecules or break chemical bonds. These radiations have the ability to cause chemical reactions and damage living cells beyond that resulting from simple heating, and can be a health hazard.
Articles about
Electromagnetism

Electricity / Magnetism / Optics / History / Textbooks
show / Electrostatics
show / Magnetostatics
hide / Electrodynamics / Lorentz force law / Electromagnetic induction / Faraday's law / Lenz's law / Displacement current / Maxwell's equations / Electromagnetic field / Electromagnetic pulse / Electromagnetic radiation / Larmor formula / Bremsstrahlung / Cyclotron radiation / Synchrotron radiation / Maxwell tensor / Poynting vector / Liénard–Wiechert potential / Jefimenko's equations / Eddy current / London equations / Mathematical descriptions of the electromagnetic field
show / Electrical network
show / Magnetic circuit
show / Covariant formulation
show / Scientists

## Physics[edit]
### Theory[edit]
 light (blue, green, and red) with a distance scale in micrometers along the x-axis.
Main articles: Maxwell's equations and Near and far field
#### Maxwell's equations[edit]
James Clerk Maxwell derived a wave form of the electric and magnetic equations, thus uncovering the wave-like nature of electric and magnetic fields and their symmetry. Because the speed of EM waves predicted by the wave equation coincided with the measured speed of light, Maxwell concluded that light itself is an EM wave.[9][10] Maxwell's equations were confirmed by Heinrich Hertz through experiments with radio waves.[11]
#### Near and far fields[edit]
Main articles: Near and far field and Liénard–Wiechert potential
 electromagnetic field that radiate into infinite space and decrease in intensity by an inverse-square law of power, so that the total radiation energy that crosses through an imaginary spherical surface is the same, no matter how far away from the antenna the spherical surface is drawn. Electromagnetic radiation thus includes the far field part of the electromagnetic field around a transmitter. A part of the "near-field" close to the transmitter, forms part of the changing electromagnetic field, but does not count as electromagnetic radiation.
Maxwell's equations established that some charges and currents ("sources") produce a local type of electromagnetic field near them that does not radiate. Currents directly produce a magnetic field, but it is of a magnetic dipole type that dies out with distance from the current. In a similar manner, moving charges pushed apart in a conductor by a changing electrical potential (such as in an antenna) produce an electric dipole type electrical field, but this also declines with distance. These fields make up the near-field near the EMR source. Neither of these behaviours are responsible for EM radiation. Instead, they cause electromagnetic field behaviour that only efficiently transfers power to a receiver very close to the source, such as the magnetic induction inside a transformer. Typically, near-fields have a powerful effect on their own sources, causing an increased "load" (decreased electrical reactance) in the source or transmitter, whenever energy is withdrawn from the EM field by a receiver. Otherwise, these fields do not "propagate" freely out into space, carrying their energy away without distance-limit, but rather oscillate, returning their energy to the transmitter if it is not received by a receiver.[citation needed]
By contrast, the EM far-field is composed of radiation that is free of the transmitter in the sense that (unlike the case in an electrical transformer) the transmitter requires the same power to send these changes in the fields out, whether the signal is immediately picked up or not. This distant part of the electromagnetic field is "electromagnetic radiation" (also called the far-field). The far-fields propagate (radiate) without allowing the transmitter to affect them. This causes them to be independent in the sense that their existence and their energy, after they have left the transmitter, is completely independent of both transmitter and receiver. Due to conservation of energy, the amount of power passing through any spherical surface drawn around the source is the same. Because such a surface has an area proportional to the square of its distance from the source, the power density of EM radiation from an isotropic source decreases with the inverse square of the distance from the source; this is called the inverse-square law. This is in contrast to dipole parts of the EM field close to the source (the near-field), which vary in intensity according to an inverse cube power law, and thus do not transport a conserved amount of energy over distances, but instead fade with distance, with its energy (as noted) rapidly returning to the transmitter or absorbed by a nearby receiver (such as a transformer secondary coil).
In the Liénard–Wiechert potential formulation of the electric and magnetic fields due to motion of a single particle (according to Maxwell's equations), the terms associated with acceleration of the particle are those that are responsible for the part of the field that is regarded as electromagnetic radiation. By contrast, the term associated with the changing static electric field of the particle and the magnetic term that results from the particle's uniform velocity, are both associated with the electromagnetic near-field, and do not comprise EM radiation.[citation needed]
### Properties[edit]

Electric and magnetic fields obey the properties of superposition. Thus, a field due to any particular particle or time-varying electric or magnetic field contributes to the fields present in the same space due to other causes. Further, as they are vector fields, all magnetic and electric field vectors add together according to vector addition.[12] For example, in optics two or more coherent light waves may interact and by constructive or destructive interference yield a resultant irradiance deviating from the sum of the component irradiances of the individual light waves.[13]
The electromagnetic fields of light are not affected by traveling through static electric or magnetic fields in a linear medium such as a vacuum. However, in nonlinear media, such as some crystals, interactions can occur between light and static electric and magnetic fields—these interactions include the Faraday effect and the Kerr effect.[14][15]
In refraction, a wave crossing from one medium to another of different density alters its speed and direction upon entering the new medium. The ratio of the refractive indices of the media determines the degree of refraction, and is summarized by Snell's law. Light of composite wavelengths (natural sunlight) disperses into a visible spectrum passing through a prism, because of the wavelength-dependent refractive index of the prism material (dispersion); that is, each component wave within the composite light is bent a different amount.[16]
EM radiation exhibits both wave properties and particle properties at the same time (see wave-particle duality). Both wave and particle characteristics have been confirmed in many experiments. Wave characteristics are more apparent when EM radiation is measured over relatively large timescales and over large distances while particle characteristics are more evident when measuring small timescales and distances. For example, when electromagnetic radiation is absorbed by matter, particle-like properties will be more obvious when the average number of photons in the cube of the relevant wavelength is much smaller than 1. It is not so difficult to experimentally observe non-uniform deposition of energy when light is absorbed, however this alone is not evidence of "particulate" behavior. Rather, it reflects the quantum nature of matter.[17] Demonstrating that the light itself is quantized, not merely its interaction with matter, is a more subtle affair.
Some experiments display both the wave and particle natures of electromagnetic waves, such as the self-interference of a single photon.[18] When a single photon is sent through an interferometer, it passes through both paths, interfering with itself, as waves do, yet is detected by a photomultiplier or other sensitive detector only once.
A quantum theory of the interaction between electromagnetic radiation and matter such as electrons is described by the theory of quantum electrodynamics.
Electromagnetic waves can be polarized, reflected, refracted, diffracted or interfere with each other.[19][20][21]
### Wave model[edit]

In homogeneous, isotropic media, electromagnetic radiation is a transverse wave,[22] meaning that its oscillations are perpendicular to the direction of energy transfer and travel. It comes from the following equations:

These equations predicate that any electromagnetic wave must be a transverse wave, where the electric field E and the magnetic field B are both perpendicular to the direction of wave propagation.
The electric and magnetic parts of the field in an electromagnetic wave stand in a fixed ratio of strengths to satisfy the two Maxwell equations that specify how one is produced from the other. In dissipation-less (lossless) media, these E and B fields are also in phase, with both reaching maxima and minima at the same points in space (see illustrations). In the far-field EM radiation which is described by the two source-free Maxwell curl operator equations, a time-change in one type of field is proportional to the curl of the other. These derivatives require that the E and B fields in EMR are in-phase (see mathematics section below).[citation needed] An important aspect of light's nature is its frequency. The frequency of a wave is its rate of oscillation and is measured in hertz, the SI unit of frequency, where one hertz is equal to one oscillation per second. Light usually has multiple frequencies that sum to form the resultant wave. Different frequencies undergo different angles of refraction, a phenomenon known as dispersion.
A monochromatic wave (a wave of a single frequency) consists of successive troughs and crests, and the distance between two adjacent crests or troughs is called the wavelength. Waves of the electromagnetic spectrum vary in size, from very long radio waves longer than a continent to very short gamma rays smaller than atom nuclei. Frequency is inversely proportional to wavelength, according to the equation:[23]

where v is the speed of the wave (c in a vacuum or less in other media), f is the frequency and λ is the wavelength. As waves cross boundaries between different media, their speeds change but their frequencies remain constant.
Electromagnetic waves in free space must be solutions of Maxwell's electromagnetic wave equation. Two main classes of solutions are known, namely plane waves and spherical waves. The plane waves may be viewed as the limiting case of spherical waves at a very large (ideally infinite) distance from the source. Both types of waves can have a waveform which is an arbitrary time function (so long as it is sufficiently differentiable to conform to the wave equation). As with any time function, this can be decomposed by means of Fourier analysis into its frequency spectrum, or individual sinusoidal components, each of which contains a single frequency, amplitude and phase. Such a component wave is said to be monochromatic. A monochromatic electromagnetic wave can be characterized by its frequency or wavelength, its peak amplitude, its phase relative to some reference phase, its direction of propagation, and its polarization.
Interference is the superposition of two or more waves resulting in a new wave pattern. If the fields have components in the same direction, they constructively interfere, while opposite directions cause destructive interference. An example of interference caused by EMR is electromagnetic interference (EMI) or as it is more commonly known as, radio-frequency interference (RFI).[citation needed] Additionally, multiple polarization signals can be combined (i.e. interfered) to form new states of polarization, which is known as parallel polarization state generation.[24]
The energy in electromagnetic waves is sometimes called radiant energy.[25][26][27]
### Particle model and quantum theory[edit]
See also: Quantization (physics) and Quantum optics
An anomaly arose in the late 19th century involving a contradiction between the wave theory of light and measurements of the electromagnetic spectra that were being emitted by thermal radiators known as black bodies. Physicists struggled with this problem unsuccessfully for many years, and it later became known as the ultraviolet catastrophe. In 1900, Max Planck developed a new theory of black-body radiation that explained the observed spectrum. Planck's theory was based on the idea that black bodies emit light (and other electromagnetic radiation) only as discrete bundles or packets of energy. These packets were called quanta. In 1905, Albert Einstein proposed that light quanta be regarded as real particles. Later the particle of light was given the name photon, to correspond with other particles being described around this time, such as the electron and proton. A photon has an energy, E, proportional to its frequency, f, by

where h is Planck's constant,  is the wavelength and c is the speed of light. This is sometimes known as the Planck–Einstein equation.[28] In quantum theory (see first quantization) the energy of the photons is thus directly proportional to the frequency of the EMR wave.[29]

Likewise, the momentum p of a photon is also proportional to its frequency and inversely proportional to its wavelength:

The source of Einstein's proposal that light was composed of particles (or could act as particles in some circumstances) was an experimental anomaly not explained by the wave theory: the photoelectric effect, in which light striking a metal surface ejected electrons from the surface, causing an electric current to flow across an applied voltage. Experimental measurements demonstrated that the energy of individual ejected electrons was proportional to the frequency, rather than the intensity, of the light. Furthermore, below a certain minimum frequency, which depended on the particular metal, no current would flow regardless of the intensity. These observations appeared to contradict the wave theory, and for years physicists tried in vain to find an explanation. In 1905, Einstein explained this puzzle by resurrecting the particle theory of light to explain the observed effect. Because of the preponderance of evidence in favor of the wave theory, however, Einstein's ideas were met initially with great skepticism among established physicists. Eventually Einstein's explanation was accepted as new particle-like behavior of light was observed, such as the Compton effect.[30][31]
As a photon is absorbed by an atom, it excites the atom, elevating an electron to a higher energy level (one that is on average farther from the nucleus). When an electron in an excited molecule or atom descends to a lower energy level, it emits a photon of light at a frequency corresponding to the energy difference. Since the energy levels of electrons in atoms are discrete, each element and each molecule emits and absorbs its own characteristic frequencies. Immediate photon emission is called fluorescence, a type of photoluminescence. An example is visible light emitted from fluorescent paints, in response to ultraviolet (blacklight). Many other fluorescent emissions are known in spectral bands other than visible light. Delayed emission is called phosphorescence.[32][33]
### Wave–particle duality[edit]
Main article: Wave–particle duality
The modern theory that explains the nature of light includes the notion of wave–particle duality.
### Wave and particle effects of electromagnetic radiation[edit]
Together, wave and particle effects fully explain the emission and absorption spectra of EM radiation. The matter-composition of the medium through which the light travels determines the nature of the absorption and emission spectrum. These bands correspond to the allowed energy levels in the atoms. Dark bands in the absorption spectrum are due to the atoms in an intervening medium between source and observer. The atoms absorb certain frequencies of the light between emitter and detector/eye, then emit them in all directions. A dark band appears to the detector, due to the radiation scattered out of the light beam. For instance, dark bands in the light emitted by a distant star are due to the atoms in the star's atmosphere. A similar phenomenon occurs for emission, which is seen when an emitting gas glows due to excitation of the atoms from any mechanism, including heat. As electrons descend to lower energy levels, a spectrum is emitted that represents the jumps between the energy levels of the electrons, but lines are seen because again emission happens only at particular energies after excitation.[34] An example is the emission spectrum of nebulae.[citation needed] Rapidly moving electrons are most sharply accelerated when they encounter a region of force, so they are responsible for producing much of the highest frequency electromagnetic radiation observed in nature.
These phenomena can aid various chemical determinations for the composition of gases lit from behind (absorption spectra) and for glowing gases (emission spectra). Spectroscopy (for example) determines what chemical elements comprise a particular star. Spectroscopy is also used in the determination of the distance of a star, using the red shift.[35]
### Propagation speed[edit]
Main article: Speed of light
When any wire (or other conducting object such as an antenna) conducts alternating current, electromagnetic radiation is propagated at the same frequency as the current.
As a wave, light is characterized by a velocity (the speed of light), wavelength, and frequency. As particles, light is a stream of photons. Each has an energy related to the frequency of the wave given by Planck's relation E = hf, where E is the energy of the photon, h is Planck's constant, 6.626 × 10−34 J·s, and f is the frequency of the wave.[36]
In a medium (other than vacuum), velocity factor or refractive index are considered, depending on frequency and application. Both of these are ratios of the speed in a medium to speed in a vacuum.
## History of discovery[edit]
See also: History of electromagnetic theory, Timeline of electromagnetism and classical optics, and Radiation § Discovery
Electromagnetic radiation of wavelengths other than those of visible light were discovered in the early 19th century. The discovery of infrared radiation is ascribed to astronomer William Herschel, who published his results in 1800 before the Royal Society of London.[37] Herschel used a glass prism to refract light from the Sun and detected invisible rays that caused heating beyond the red part of the spectrum, through an increase in the temperature recorded with a thermometer. These "calorific rays" were later termed infrared.[38]
In 1801, German physicist Johann Wilhelm Ritter discovered ultraviolet in an experiment similar to Herschel's, using sunlight and a glass prism. Ritter noted that invisible rays near the violet edge of a solar spectrum dispersed by a triangular prism darkened silver chloride preparations more quickly than did the nearby violet light. Ritter's experiments were an early precursor to what would become photography. Ritter noted that the ultraviolet rays (which at first were called "chemical rays") were capable of causing chemical reactions.[39][40]
James Clerk Maxwell
In 1862–64 James Clerk Maxwell developed equations for the electromagnetic field which suggested that waves in the field would travel with a speed that was very close to the known speed of light. Maxwell therefore suggested that visible light (as well as invisible infrared and ultraviolet rays by inference) all consisted of propagating disturbances (or radiation) in the electromagnetic field. Radio waves were first produced deliberately by Heinrich Hertz in 1887, using electrical circuits calculated to produce oscillations at a much lower frequency than that of visible light, following recipes for producing oscillating charges and currents suggested by Maxwell's equations. Hertz also developed ways to detect these waves, and produced and characterized what were later termed radio waves and microwaves.[41]: 286, 7
Wilhelm Röntgen discovered and named X-rays. After experimenting with high voltages applied to an evacuated tube on 8 November 1895, he noticed a fluorescence on a nearby plate of coated glass. In one month, he discovered X-rays' main properties.[41]: 307
The last portion of the EM spectrum to be discovered was associated with radioactivity. Henri Becquerel found that uranium salts caused fogging of an unexposed photographic plate through a covering paper in a manner similar to X-rays, and Marie Curie discovered that only certain elements gave off these rays of energy, soon discovering the intense radiation of radium. The radiation from pitchblende was differentiated into alpha rays (alpha particles) and beta rays (beta particles) by Ernest Rutherford through simple experimentation in 1899, but these proved to be charged particulate types of radiation. However, in 1900 the French scientist Paul Villard discovered a third neutrally charged and especially penetrating type of radiation from radium, and after he described it, Rutherford realized it must be yet a third type of radiation, which in 1903 Rutherford named gamma rays. In 1910 British physicist William Henry Bragg demonstrated that gamma rays are electromagnetic radiation, not particles, and in 1914 Rutherford and Edward Andrade measured their wavelengths, finding that they were similar to X-rays but with shorter wavelengths and higher frequency, although a 'cross-over' between X and gamma rays makes it possible to have X-rays with a higher energy (and hence shorter wavelength) than gamma rays and vice versa. The origin of the ray differentiates them, gamma rays tend to be natural phenomena originating from the unstable nucleus of an atom and X-rays are electrically generated (and hence man-made) unless they are as a result of bremsstrahlung X-radiation caused by the interaction of fast moving particles (such as beta particles) colliding with certain materials, usually of higher atomic numbers.[41]: 308, 9
## Electromagnetic spectrum[edit]
Main article: Electromagnetic spectrum
Electromagnetic spectrum with visible light highlightedLegend:
γ = Gamma rays
HX = Hard X-rays
SX = Soft X-Rays
EUV = Extreme-ultraviolet
NUV = Near-ultraviolet
Visible light (colored bands)
NIR = Near-infrared
MIR = Mid-infrared
FIR = Far-infrared
EHF = Extremely high frequency (microwaves)
SHF = Super-high frequency (microwaves)
UHF = Ultrahigh frequency (radio waves)
VHF = Very high frequency (radio)
HF = High frequency (radio)
MF = Medium frequency (radio)
LF = Low frequency (radio)
VLF = Very low frequency (radio)
VF = Voice frequency
ULF = Ultra-low frequency (radio)
SLF = Super-low frequency (radio)
ELF = Extremely low frequency (radio)
EM radiation (the designation 'radiation' excludes static electric and magnetic and near fields) is classified by wavelength into radio, microwave, infrared, visible, ultraviolet, X-rays and gamma rays. Arbitrary electromagnetic waves can be expressed by Fourier analysis in terms of sinusoidal monochromatic waves, which in turn can each be classified into these regions of the EMR spectrum.
For certain classes of EM waves, the waveform is most usefully treated as random, and then spectral analysis must be done by slightly different mathematical techniques appropriate to random or stochastic processes. In such cases, the individual frequency components are represented in terms of their power content, and the phase information is not preserved. Such a representation is called the power spectral density of the random process. Random electromagnetic radiation requiring this kind of analysis is, for example, encountered in the interior of stars, and in certain other very wideband forms of radiation such as the Zero point wave field of the electromagnetic vacuum.
The behavior of EM radiation and its interaction with matter depends on its frequency, and changes qualitatively as the frequency changes. Lower frequencies have longer wavelengths, and higher frequencies have shorter wavelengths, and are associated with photons of higher energy. There is no fundamental limit known to these wavelengths or energies, at either end of the spectrum, although photons with energies near the Planck energy or exceeding it (far too high to have ever been observed) will require new physical theories to describe.
### Radio and microwave[edit]
Main articles: Radio wave and Microwave
When radio waves impinge upon a conductor, they couple to the conductor, travel along it and induce an electric current on the conductor surface by moving the electrons of the conducting material in correlated bunches of charge. Such effects can cover macroscopic distances in conductors (such as radio antennas), since the wavelength of radio waves is long.
Electromagnetic radiation phenomena with wavelengths ranging from as long as one meter to as short as one millimeter are called microwaves; with frequencies between 300 MHz (0.3 GHz) and 300 GHz.
At radio and microwave frequencies, EMR interacts with matter largely as a bulk collection of charges which are spread out over large numbers of affected atoms. In electrical conductors, such induced bulk movement of charges (electric currents) results in absorption of the EMR, or else separations of charges that cause generation of new EMR (effective reflection of the EMR). An example is absorption or emission of radio waves by antennas, or absorption of microwaves by water or other molecules with an electric dipole moment, as for example inside a microwave oven. These interactions produce either electric currents or heat, or both.
### Infrared[edit]
Main article: Infrared
Like radio and microwave, infrared (IR) also is reflected by metals (and also most EMR, well into the ultraviolet range). However, unlike lower-frequency radio and microwave radiation, Infrared EMR commonly interacts with dipoles present in single molecules, which change as atoms vibrate at the ends of a single chemical bond. It is consequently absorbed by a wide range of substances, causing them to increase in temperature as the vibrations dissipate as heat. The same process, run in reverse, causes bulk substances to radiate in the infrared spontaneously (see thermal radiation section below).
Infrared radiation is divided into spectral subregions. While different subdivision schemes exist,[42][43] the spectrum is commonly divided as near-infrared (0.75–1.4 μm), short-wavelength infrared (1.4–3 μm), mid-wavelength infrared (3–8 μm), long-wavelength infrared (8–15 μm) and far infrared (15–1000 μm).[44]
### Visible light[edit]
Main article: Light
Natural sources produce EM radiation across the spectrum. EM radiation with a wavelength between approximately 400 nm and 700 nm is directly detected by the human eye and perceived as visible light. Other wavelengths, especially nearby infrared (longer than 700 nm) and ultraviolet (shorter than 400 nm) are also sometimes referred to as light.
As frequency increases into the visible range, photons have enough energy to change the bond structure of some individual molecules. It is not a coincidence that this happens in the visible range, as the mechanism of vision involves the change in bonding of a single molecule, retinal, which absorbs a single photon. The change in retinal causes a change in the shape of the rhodopsin protein it is contained in, which starts the biochemical process that causes the retina of the human eye to sense the light.
Photosynthesis becomes possible in this range as well, for the same reason. A single molecule of chlorophyll is excited by a single photon. In plant tissues that conduct photosynthesis, carotenoids act to quench electronically excited chlorophyll produced by visible light in a process called non-photochemical quenching, to prevent reactions that would otherwise interfere with photosynthesis at high light levels.
Animals that detect infrared make use of small packets of water that change temperature, in an essentially thermal process that involves many photons.
Infrared, microwaves and radio waves are known to damage molecules and biological tissue only by bulk heating, not excitation from single photons of the radiation.
Visible light is able to affect only a tiny percentage of all molecules. Usually not in a permanent or damaging way, rather the photon excites an electron which then emits another photon when returning to its original position. This is the source of color produced by most dyes. Retinal is an exception. When a photon is absorbed, the retinal permanently changes structure from cis to trans, and requires a protein to convert it back, i.e. reset it to be able to function as a light detector again.
Limited evidence indicate that some reactive oxygen species are created by visible light in skin, and that these may have some role in photoaging, in the same manner as ultraviolet A.[45]
### Ultraviolet[edit]
Main article: Ultraviolet
As frequency increases into the ultraviolet, photons now carry enough energy (about three electron volts or more) to excite certain doubly bonded molecules into permanent chemical rearrangement. In DNA, this causes lasting damage. DNA is also indirectly damaged by reactive oxygen species produced by ultraviolet A (UVA), which has energy too low to damage DNA directly. This is why ultraviolet at all wavelengths can damage DNA, and is capable of causing cancer, and (for UVB) skin burns (sunburn) that are far worse than would be produced by simple heating (temperature increase) effects. This property of causing molecular damage that is out of proportion to heating effects, is characteristic of all EMR with frequencies at the visible light range and above. These properties of high-frequency EMR are due to quantum effects that permanently damage materials and tissues at the molecular level.[citation needed]
At the higher end of the ultraviolet range, the energy of photons becomes large enough to impart enough energy to electrons to cause them to be liberated from the atom, in a process called photoionisation. The energy required for this is always larger than about 10 electron volt (eV) corresponding with wavelengths smaller than 124 nm (some sources suggest a more realistic cutoff of 33 eV, which is the energy required to ionize water). This high end of the ultraviolet spectrum with energies in the approximate ionization range, is sometimes called "extreme UV." Ionizing UV is strongly filtered by the Earth's atmosphere.[citation needed]
### X-rays and gamma rays[edit]
Main articles: X-rays and Gamma rays
Electromagnetic radiation composed of photons that carry minimum-ionization energy, or more, (which includes the entire spectrum with shorter wavelengths), is therefore termed ionizing radiation. (Many other kinds of ionizing radiation are made of non-EM particles). Electromagnetic-type ionizing radiation extends from the extreme ultraviolet to all higher frequencies and shorter wavelengths, which means that all X-rays and gamma rays qualify. These are capable of the most severe types of molecular damage, which can happen in biology to any type of biomolecule, including mutation and cancer, and often at great depths below the skin, since the higher end of the X-ray spectrum, and all of the gamma ray spectrum, penetrate matter.
## Atmosphere and magnetosphere[edit]
Main articles: ozone layer, shortwave radio, skywave, and ionosphere
 opacity) of various wavelengths of electromagnetic radiation
Most UV and X-rays are blocked by absorption first from molecular nitrogen, and then (for wavelengths in the upper UV) from the electronic excitation of dioxygen and finally ozone at the mid-range of UV. Only 30% of the Sun's ultraviolet light reaches the ground, and almost all of this is well transmitted.
Visible light is well transmitted in air, as it is not energetic enough to excite nitrogen, oxygen, or ozone, but too energetic to excite molecular vibrational frequencies of water vapor.[citation needed]
Absorption bands in the infrared are due to modes of vibrational excitation in water vapor. However, at energies too low to excite water vapor, the atmosphere becomes transparent again, allowing free transmission of most microwave and radio waves. [46]
Finally, at radio wavelengths longer than 10 m or so (about 30 MHz), the air in the lower atmosphere remains transparent to radio, but plasma in certain layers of the ionosphere begins to interact with radio waves (see skywave). This property allows some longer wavelengths (100 m or 3 MHz) to be reflected and results in shortwave radio beyond line-of-sight. However, certain ionospheric effects begin to block incoming radiowaves from space, when their frequency is less than about 10 MHz (wavelength longer than about 30 m).[47]
## Thermal and electromagnetic radiation as a form of heat[edit]
Main articles: Thermal radiation and Planck's law
The basic structure of matter involves charged particles bound together. When electromagnetic radiation impinges on matter, it causes the charged particles to oscillate and gain energy. The ultimate fate of this energy depends on the context. It could be immediately re-radiated and appear as scattered, reflected, or transmitted radiation. It may get dissipated into other microscopic motions within the matter, coming to thermal equilibrium and manifesting itself as thermal energy, or even kinetic energy, in the material. With a few exceptions related to high-energy photons (such as fluorescence, harmonic generation, photochemical reactions, the photovoltaic effect for ionizing radiations at far ultraviolet, X-ray and gamma radiation), absorbed electromagnetic radiation simply deposits its energy by heating the material. This happens for infrared, microwave and radio wave radiation. Intense radio waves can thermally burn living tissue and can cook food. In addition to infrared lasers, sufficiently intense visible and ultraviolet lasers can easily set paper afire.[48]
Ionizing radiation creates high-speed electrons in a material and breaks chemical bonds, but after these electrons collide many times with other atoms eventually most of the energy becomes thermal energy all in a tiny fraction of a second. This process makes ionizing radiation far more dangerous per unit of energy than non-ionizing radiation. This caveat also applies to UV, even though almost all of it is not ionizing, because UV can damage molecules due to electronic excitation, which is far greater per unit energy than heating effects.[48][citation needed]
Infrared radiation in the spectral distribution of a black body is usually considered a form of heat, since it has an equivalent temperature and is associated with an entropy change per unit of thermal energy. However, "heat" is a technical term in physics and thermodynamics and is often confused with thermal energy. Any type of electromagnetic energy can be transformed into thermal energy in interaction with matter. Thus, any electromagnetic radiation can "heat" (in the sense of increase the thermal energy temperature of) a material, when it is absorbed.[49]
The inverse or time-reversed process of absorption is thermal radiation. Much of the thermal energy in matter consists of random motion of charged particles, and this energy can be radiated away from the matter. The resulting radiation may subsequently be absorbed by another piece of matter, with the deposited energy heating the material.[50]
The electromagnetic radiation in an opaque cavity at thermal equilibrium is effectively a form of thermal energy, having maximum radiation entropy.[51]
## Biological effects[edit]
Main articles: Electromagnetic radiation and health and Wireless device radiation and health
Bioelectromagnetics is the study of the interactions and effects of EM radiation on living organisms. The effects of electromagnetic radiation upon living cells, including those in humans, depends upon the radiation's power and frequency. For low-frequency radiation (radio waves to visible light) the best-understood effects are those due to radiation power alone, acting through heating when radiation is absorbed. For these thermal effects, frequency is important as it affects the intensity of the radiation and penetration into the organism (for example, microwaves penetrate better than infrared). It is widely accepted that low frequency fields that are too weak to cause significant heating could not possibly have any biological effect.[52]
Some research suggests that weaker non-thermal electromagnetic fields (including weak ELF magnetic fields, although the latter does not strictly qualify as EM radiation[52][53][54]) and modulated RF and microwave fields can have biological effects, though the significance of this is unclear.[55][56]
The World Health Organization has classified radio frequency electromagnetic radiation as Group 2B – possibly carcinogenic.[57][58] This group contains possible carcinogens such as lead, DDT, and styrene. For example, epidemiological studies looking for a relationship between cell phone use and brain cancer development have been largely inconclusive, save to demonstrate that the effect, if it exists, cannot be a large one.
At higher frequencies (visible and beyond), the effects of individual photons begin to become important, as these now have enough energy individually to directly or indirectly damage biological molecules.[59] All UV frequencies have been classed as Group 1 carcinogens by the World Health Organization. Ultraviolet radiation from sun exposure is the primary cause of skin cancer.[60][61]
Thus, at UV frequencies and higher (and probably somewhat also in the visible range),[45] electromagnetic radiation does more damage to biological systems than simple heating predicts. This is most obvious in the "far" (or "extreme") ultraviolet. UV, with X-ray and gamma radiation, are referred to as ionizing radiation due to the ability of photons of this radiation to produce ions and free radicals in materials (including living tissue). Since such radiation can severely damage life at energy levels that produce little heating, it is considered far more dangerous (in terms of damage-produced per unit of energy, or power) than the rest of the electromagnetic spectrum.
### Use as a weapon[edit]
See also: Directed energy weapons § Microwave weapons
The heat ray is an application of EMR that makes use of microwave frequencies to create an unpleasant heating effect in the upper layer of the skin. A publicly known heat ray weapon called the Active Denial System was developed by the US military as an experimental weapon to deny the enemy access to an area.[62] A death ray is a theoretical weapon that delivers heat ray based on electromagnetic energy at levels that are capable of injuring human tissue. An inventor of a death ray, Harry Grindell Matthews, claimed to have lost sight in his left eye while working on his death ray weapon based on a microwave magnetron from the 1920s (a normal microwave oven creates a tissue damaging cooking effect inside the oven at around 2 kV/m).[63]
## Derivation from electromagnetic theory[edit]
Main article: Electromagnetic wave equation
Electromagnetic waves are predicted by the classical laws of electricity and magnetism, known as Maxwell's equations. There are nontrivial solutions of the homogeneous Maxwell's equations (without charges or currents), describing waves of changing electric and magnetic fields. Beginning with Maxwell's equations in free space:
(1)

(2)

(3)

(4)

where
- and  are the electric field (measured in V/m or N/C) and the magnetic field (measured in T or Wb/m2), respectively;

- yields the divergence and  the curl of a vector field

- and  are partial derivatives (rate of change in time, with location fixed) of the magnetic and electric field;

- is the permeability of a vacuum (4π × 10−7 (H/m)), and  is the permittivity of a vacuum (8.85×10−12 (F/m));

Besides the trivial solution

useful solutions can be derived with the following vector identity, valid for all vectors  in some vector field:

Taking the curl of the second Maxwell equation (2) yields:
(5)

Evaluating the left hand side of (5) with the above identity and simplifying using (1), yields:
(6)

Evaluating the right hand side of (5) by exchanging the sequence of derivations and inserting the fourth Maxwell equation (4), yields:
(7)

Combining (6) and (7) again, gives a vector-valued differential equation for the electric field, solving the homogeneous Maxwell equations:

Taking the curl of the fourth Maxwell equation (4) results in a similar differential equation for a magnetic field solving the homogeneous Maxwell equations:

Both differential equations have the form of the general wave equation for waves propagating with speed  where  is a function of time and location, which gives the amplitude of the wave at some time at a certain location:

This is also written as:

where  denotes the so-called d'Alembert operator, which in Cartesian coordinates is given as:

Comparing the terms for the speed of propagation, yields in the case of the electric and magnetic fields:

This is the speed of light in vacuum. Thus Maxwell's equations connect the vacuum permittivity , the vacuum permeability , and the speed of light, c0, via the above equation. This relationship had been discovered by Wilhelm Eduard Weber and Rudolf Kohlrausch prior to the development of Maxwell's electrodynamics, however Maxwell was the first to produce a field theory consistent with waves traveling at the speed of light.

These are only two equations versus the original four, so more information pertains to these waves hidden within Maxwell's equations. A generic vector wave for the electric field has the form

Here,  is the constant amplitude,  is any second differentiable function,  is a unit vector in the direction of propagation, and  is a position vector.  is a generic solution to the wave equation. In other words,

for a generic wave traveling in the  direction.

From the first of Maxwell's equations, we get

Thus,

which implies that the electric field is orthogonal to the direction the wave propagates. The second of Maxwell's equations yields the magnetic field, namely,

Thus,

The remaining equations will be satisfied by this choice of .

The electric and magnetic field waves in the far-field travel at the speed of light. They have a special restricted orientation and proportional magnitudes, , which can be seen immediately from the Poynting vector. The electric field, magnetic field, and direction of wave propagation are all orthogonal, and the wave propagates in the same direction as . Also, E and B far-fields in free space, which as wave solutions depend primarily on these two Maxwell equations, are in-phase with each other. This is guaranteed since the generic wave solution is first order in both space and time, and the curl operator on one side of these equations results in first-order spatial derivatives of the wave solution, while the time-derivative on the other side of the equations, which gives the other field, is first-order in time, resulting in the same phase shift for both fields in each mathematical operation.

From the viewpoint of an electromagnetic wave traveling forward, the electric field might be oscillating up and down, while the magnetic field oscillates right and left. This picture can be rotated with the electric field oscillating right and left and the magnetic field oscillating down and up. This is a different solution that is traveling in the same direction. This arbitrariness in the orientation with respect to propagation direction is known as polarization. On a quantum level, it is described as photon polarization. The direction of the polarization is defined as the direction of the electric field.
More general forms of the second-order wave equations given above are available, allowing for both non-vacuum propagation media and sources. Many competing derivations exist, all with varying levels of approximation and intended applications. One very general example is a form of the electric field equation,[64] which was factorized into a pair of explicitly directional wave equations, and then efficiently reduced into a single uni-directional wave equation by means of a simple slow-evolution approximation.
## See also[edit]
- Antenna measurement
- Bioelectromagnetics
- Bolometer
- CONELRAD
- Electromagnetic pulse
- Electromagnetic radiation and health
- Evanescent wave coupling
- Finite-difference time-domain method
- Gravitational wave
- Helicon
- Impedance of free space
- Radiation reaction
- Health effects of sunlight exposure
- Sinusoidal plane-wave solutions of the electromagnetic wave equation
## References[edit]
1. ^ *Purcell and Morin, Harvard University. (2013). Electricity and Magnetism, 820p (3rd ed.). Cambridge University Press, New York. ISBN . p 430: "These waves... require no medium to support their propagation. Traveling electromagnetic waves carry energy, and... the Poynting vector describes the energy flow...;" p 440: ... the electromagnetic wave must have the following properties: 1) The field pattern travels with speed c (speed of light); 2) At every point within the wave... the electric field strength E equals "c" times the magnetic field strength B; 3) The electric field and the magnetic field are perpendicular to one another and to the direction of travel, or propagation."
2. ^ * Browne, Michael (2013). Physics for Engineering and Science, p427 (2nd ed.). McGraw Hill/Schaum, New York. ISBN .; p319: "For historical reasons, different portions of the EM spectrum are given different names, although they are all the same kind of thing. Visible light constitutes a narrow range of the spectrum, from wavelengths of about 400-800 nm.... ;p 320 "An electromagnetic wave carries forward momentum... If the radiation is absorbed by a surface, the momentum drops to zero and a force is exerted on the surface... Thus the radiation pressure of an electromagnetic wave is (formula)."
3. ^ Maxwell, J. Clerk (1 January 1865). "A Dynamical Theory of the Electromagnetic Field". Philosophical Transactions of the Royal Society of London. 155: 459–512. Bibcode:1865RSPT..155..459C. doi:10.1098/rstl.1865.0008. S2CID 186207827.
4. ^ Cloude, Shane (1995). An Introduction to Electromagnetic Wave Propagation and Antennas. Springer Science and Business Media. pp. 28–33. ISBN .
5. ^ Bettini, Alessandro (2016). A Course in Classical Physics, Vol. 4 – Waves and Light. Springer. pp. 95, 103. ISBN .
6. ^ "The Dual Nature of Light as Reflected in the Nobel Archives". nobelprize.org. Archived from the original on 15 July 2017. Retrieved 4 September 2017.
7. ^ "Electromagnetic Spectrum facts, information, pictures | Encyclopedia.com articles about Electromagnetic Spectrum". encyclopedia.com. Archived from the original on 13 June 2017. Retrieved 4 September 2017.
8. ^ Tipler, Paul A. (1999). Physics for Scientists and Engineers: Vol. 1: Mechanics, Oscillations and Waves, Thermodynamics. MacMillan. p. 454. ISBN .
9. ^ Elert, Glenn. "Electromagnetic Waves". The Physics Hypertextbook. Retrieved 4 June 2018.
10. ^ "The Impact of James Clerk Maxwell's Work". clerkmaxwellfoundation.org. Archived from the original on 17 September 2017. Retrieved 4 September 2017.
11. ^ "Maxwell's equations and the secrets of nature". plus.maths.org. 18 December 2015. Retrieved 2 May 2021.
12. ^ Purcell, p442: "Any number of electromagnetic waves can propagate through the same region without affecting one another. The field E at a space time point is the vector sum of the electric fields of the individual waves, and the same goes for B".
13. ^ "PV Performance Modeling Collaborative | Plane of Array (POA) Irradiance". Retrieved 14 January 2022.
14. ^ Chen, Szu-yuan; Maksimchuk, Anatoly; Umstadter, Donald (17 December 1998). "Experimental observation of relativistic nonlinear Thomson scattering". Nature. 396 (6712): 653–655. arXiv:physics/9810036. Bibcode:1998Natur.396..653C. doi:10.1038/25303. S2CID 16080209.
15. ^ Crowther, James Arnold (1920). The life and discoveries of Michael Faraday. Society for promoting Christian knowledge. pp. 54–57. Retrieved 15 June 2014.
16. ^ "Prisms". Spectroscopy. Spectroscopy-09-01-2008. 23 (9). September 2008. Retrieved 17 January 2021.
17. ^ Carmichael, H. J. "Einstein and the Photoelectric Effect" (PDF). Quantum Optics Theory Group, University of Auckland. Archived from the original (PDF) on 27 June 2007. Retrieved 22 December 2009.
18. ^ Thorn, J. J.; Neel, M. S.; Donato, V. W.; Bergreen, G. S.; Davies, R. E.; Beck, M. (2004). "Observing the quantum behavior of light in an undergraduate laboratory" (PDF). American Journal of Physics. 72 (9): 1210. Bibcode:2004AmJPh..72.1210T. doi:10.1119/1.1737397. Archived (PDF) from the original on 1 February 2016.
19. ^ "DATE". galileo.phys.virginia.edu. Archived from the original on 12 May 2015. Retrieved 4 September 2017.
20. ^ "Physics – Waves". www-jcsu.jesus.cam.ac.uk. Archived from the original on 4 September 2017. Retrieved 4 September 2017.
21. ^ "Wave Behaviors | Science Mission Directorate". science.nasa.gov. Archived from the original on 14 May 2017. Retrieved 4 September 2017.
22. ^ Stratton, Julius Adams (1941). "Chapter V Plane waves in unbounded, isotropic media". Electromagnetic Theory. McGraw-Hill Book Company, New York, NY. ISBN .
23. ^ "Electromagnetic Radiation | COSMOS". astronomy.swin.edu.au. Retrieved 29 March 2020.
24. ^ She, Alan; Capasso, Federico (17 May 2016). "Parallel Polarization State Generation". Scientific Reports. 6: 26019. arXiv:1602.04463. Bibcode:2016NatSR...626019S. doi:10.1038/srep26019. PMC 4869035. PMID 27184813.
25. ^ "What Is Electromagnetic Radiation?". Live Science. Archived from the original on 4 September 2017. Retrieved 4 September 2017.
26. ^ Schneiderman, Jill (27 March 2000). The Earth Around Us: Maintaining A Livable Planet. Henry Holt and Company. ISBN .
27. ^ The Michigan Technic. UM Libraries. 1960.
28. ^ Paul M. S. Monk (2004). Physical Chemistry. John Wiley and Sons. p. 435. ISBN .
29. ^ Weinberg, S. (1995). The Quantum Theory of Fields. Vol. 1. Cambridge University Press. pp. 15–17. ISBN .
30. ^ Commins, Eugene (2014). Quantum Mechanics; An Experimentalist's Approach. Cambridge University Press. ISBN .
31. ^ Ling, Samuel J.; Sanny, Jeff; Moebs, William (2016). "The Compton Effect". University physics. Volume 3. OpenStax. ISBN .
32. ^ Haneef, Deena T. Kochunni, Jazir. "7 Differences between Fluorescence and Phosphorescence". Archived from the original on 4 September 2017. Retrieved 4 September 2017.
33. ^ Meredith, W. J.; Massey, J. B. (22 October 2013). Fundamental Physics of Radiology. Butterworth-Heinemann. ISBN .
34. ^ Browne, p 376: "Radiation is emitted or absorbed only when the electron jumps from one orbit to the other, and the frequency of radiation depends only upon on the energies of the electron in the initial and final orbits.
35. ^ "Spectroscopy". National Redshift Project. National Redshift Project. Archived from the original on 1 February 2017. Retrieved 19 January 2017.
36. ^ Jones, Erick (2007). RFID in Logistics A Practical Introduction. CRC Press. p. 437. ISBN .
37. ^ Herschel, William (1 January 1800). "Experiments on the Refrangibility of the Invisible Rays of the Sun. By William Herschel, LL. D. F. R. S". Philosophical Transactions of the Royal Society of London. 90: 284–292. Bibcode:1800RSPT...90..284H. doi:10.1098/rstl.1800.0015. JSTOR 107057.
38. ^ Holzer, Aton M.; Elmets, Craig A. (2010). "The Other End of the Rainbow: Infrared and Skin". The Journal of Investigative Dermatology. 130 (6): 1496–1499. doi:10.1038/jid.2010.79. ISSN 0022-202X. PMC 2926798. PMID 20463675.
39. ^ "Ultraviolet | COSMOS". astronomy.swin.edu.au. Archived from the original on 1 March 2021. Retrieved 29 September 2021.
40. ^ Davidson, Michael W. (March 2014). "Pioneers in Optics: Johann Wilhelm Ritter and Ernest Rutherford". Microscopy Today. 22 (2): 48–51. doi:10.1017/S1551929514000029. ISSN 1551-9295. S2CID 135584871.
41. ^ Jump up to:a b c Jeans, James (1947) The Growth of Physical Science. Cambridge University Press
42. ^ Henderson, Roy. "Wavelength considerations". Instituts für Umform- und Hochleistungs. Archived from the original on 28 October 2007. Retrieved 18 October 2007.
43. ^ "Near, Mid and Far-Infrared". NASA IPAC. Archived from the original on 29 May 2012. Retrieved 4 April 2007.
44. ^ Byrnes, James (2009). Unexploded Ordnance Detection and Mitigation. Springer. pp. 21–22. Bibcode:2009uodm.book.....B. ISBN .
45. ^ Jump up to:a b Liebel, F.; Kaur, S.; Ruvolo, E.; Kollias, N.; Southall, M. D. (2012). "Irradiation of Skin with Visible Light Induces Reactive Oxygen Species and Matrix-Degrading Enzymes". Journal of Investigative Dermatology. 132 (7): 1901–1907. doi:10.1038/jid.2011.476. PMID 22318388.
46. ^ Chaplin, Martin (15 May 2013). "Infared Spectroscopy" (PDF): water.lsbu.ac.uk. Retrieved 19 April 2022.
47. ^ Dabas, R S (July 2000). "Ionosphere and its influence on radio communications". Resonance. 5 (7): 28–43. doi:10.1007/bf02867245. ISSN 0971-8044. S2CID 121347063.
48. ^ Jump up to:a b "CANDU textbook". nuceng.ca. Archived from the original on 20 April 2017. Retrieved 24 March 2017.
49. ^ "Blackbody Radiation". docs.kde.org. Archived from the original on 8 August 2017. Retrieved 24 March 2017.
50. ^ "Thermodynamics Part 1: Work, Heat, Internal Energy and Enthalpy". www2.southeastern.edu. Archived from the original on 24 March 2017. Retrieved 24 March 2017.
51. ^ "Planck's law" (PDF). astro.lu.se. Archived from the original (PDF) on 30 November 2016. Retrieved 24 March 2017.
52. ^ Jump up to:a b Binhi, Vladimir N (2002). Magnetobiology: Underlying Physical Problems. Repiev, A & Edelev, M (translators from Russian). San Diego: Academic Press. pp. 1–16. ISBN . OCLC 49700531.
53. ^ Delgado, J. M.; Leal, J.; Monteagudo, J. L.; Gracia, M. G. (1982). "Embryological changes induced by weak, extremely low frequency electromagnetic fields". Journal of Anatomy. 134 (Pt 3): 533–551. PMC 1167891. PMID 7107514.
54. ^ Harland, J. D.; Liburdy, R. P. (1997). "Environmental magnetic fields inhibit the antiproliferative action of tamoxifen and melatonin in a human breast cancer cell line". Bioelectromagnetics. 18 (8): 555–562. doi:10.1002/(SICI)1521-186X(1997)18:8<555::AID-BEM4>3.0.CO;2-1. PMID 9383244.
55. ^ Aalto, S.; Haarala, C.; Brück, A.; Sipilä, H.; Hämäläinen, H.; Rinne, J. O. (2006). "Mobile phone affects cerebral blood flow in humans". Journal of Cerebral Blood Flow & Metabolism. 26 (7): 885–890. doi:10.1038/sj.jcbfm.9600279. PMID 16495939.
56. ^ Cleary, S. F.; Liu, L. M.; Merchant, R. E. (1990). "In vitro lymphocyte proliferation induced by radio-frequency electromagnetic radiation under isothermal conditions". Bioelectromagnetics. 11 (1): 47–56. doi:10.1002/bem.2250110107. PMID 2346507.
57. ^ IARC classifies Radiofrequency Electromagnetic Fields as possibly carcinogenic to humans Archived 1 June 2011 at the Wayback Machine. World Health Organization. 31 May 2011
58. ^ "Trouble with cell phone radiation standard". CBS News. Archived from the original on 9 May 2013.
59. ^ See Liebel, F; Kaur, S; Ruvolo, E; Kollias, N; Southall, M. D. (July 2012). "Irradiation of skin with visible light induces reactive oxygen species and matrix-degrading enzymes". J. Invest. Dermatol. 132 (7): 1901–7. doi:10.1038/jid.2011.476. PMID 22318388. for evidence of quantum damage from visible light via reactive oxygen species generated in skin. This happens also with UVA. With UVB, the damage to DNA becomes direct, with photochemical formation of pyrimidine dimers.
60. ^ Narayanan, DL; Saladi, RN; Fox, JL (September 2010). "Ultraviolet radiation and skin cancer". International Journal of Dermatology. 49 (9): 978–86. doi:10.1111/j.1365-4632.2010.04474.x. PMID 20883261. S2CID 22224492.
61. ^ Saladi, RN; Persaud, AN (January 2005). "The causes of skin cancer: a comprehensive review". Drugs of Today. 41 (1): 37–53. doi:10.1358/dot.2005.41.1.875777. PMID 15753968.
62. ^ "DVIDS – News – New Marine Corps non-lethal weapon heats things up". DVIDS. Retrieved 1 November 2014.
63. ^ "Effects on the human body: Extremely low frequency RF | Radio Frequency | Radio Spectrum". Scribd. Retrieved 8 March 2021.
64. ^ Kinsler, P. (2010). "Optical pulse propagation with minimal approximations". Phys. Rev. A. 81 (1): 013819. arXiv:0810.5689. Bibcode:2010PhRvA..81a3819K. doi:10.1103/PhysRevA.81.013819.
"Light: Electromagnetic waves, the electromagnetic spectrum and photons (article)". Khan Academy. Retrieved 2 May 2021.
## Further reading[edit]
- Hecht, Eugene (2001). Optics (4th ed.). Pearson Education. ISBN .
- Serway, Raymond A.; Jewett, John W. (2004). Physics for Scientists and Engineers (6th ed.). Brooks Cole. ISBN .
- Tipler, Paul (2004). Physics for Scientists and Engineers: Electricity, Magnetism, Light, and Elementary Modern Physics (5th ed.). W. H. Freeman. ISBN .
- Reitz, John; Milford, Frederick; Christy, Robert (1992). Foundations of Electromagnetic Theory (4th ed.). Addison Wesley. ISBN .
- Jackson, John David (1999). Classical Electrodynamics (3rd ed.). John Wiley & Sons. ISBN .
- Allen Taflove and Susan C. Hagness (2005). Computational Electrodynamics: The Finite-Difference Time-Domain Method, 3rd ed. Artech House Publishers. ISBN .